InfiniBand ibtools commands	Omni-Path opa commands
Local commands
ibstatus / ibstat / ibv_devinfo, ibv_devices	opainfo / ibstat(some limitations) / ibv_devinfo, ibv_devices(MTU >= 4K shows as 4K) / hfi1_control -iv
ibportstate	opaportinfo / opaportconfig
Whole-fabric commands
ibdiagnet	opareport-o all
ibnetdiscover / iblinkinfo	opareport-o links / opaextractsellinks
ibnodes / ibhosts / ibswitches / sminfo	opaextractlids / opaextractlids -F nodetype:FI / opaextractlids -F nodetype:SW / opafabricinfo / opareport -o nodes -F sm
ibqueryerrors -r / ibqueryerrors -k	opareport -o errors / opareport -o none -C

ibtracert<from lid><to lid>	opareport -o route \ -S lid:<from lid> -D lid:<to lid>

Less commonly used commands
ibroute [-M]	opareport -o linear [-o mcast]
perfquery, ibclearerrors / (I prefer ibqueryerrors, above)	opainfo -o stats / opareport -o errors / opaextractperf / opapmaquery-o geterrorcounters\ -n 0x2 [-l <lid>]
ibping	/opt/opa/tools/opaswping-t <guid>works on switches / opapmaquery -o classportinfo-l <lid> can be used as a ping to any node
ibcheckwidth	opareport -o slowlinks